Control Inalámbrico de Velocidad en Lazo
Abierto para Motor de CC
Bongiovanni Pablo1, Guanuco Luis2, Sansó Marco3, Vassia Gonzalo4
Departamento Electrónica, UTN-FRC
Cátedra Electrónica Aplicada III

1pabloabongiovanni@gmail.com
2guanucoluis@gmail.com
3sansomarco@gmail.com
4glvassia@gmail.com

Resumen— En este documento se abordará fundamentalmente la transmisión y recepción inalámbrica en modulación digital ASK. Esta será utilizada en el control a lazo abierto de la velocidad de un motor de CC mediante modulación del ancho de pulso (PWM). El flujo de datos es unidireccional y la frecuencia de trabajo se encuentra en la banda de UHF.

Abstract- This document will approach fundamently the wireless transmition and reception with an ASK digital modulation. This will be used in a open loop DC motor velocity control using Pulse With Modulation (PWM). The data flow is unidirectional and the work frecuency is in the UHF band.

Palabras clave: transmisión, modulación, ASK, inalámbrica, Control, velocidad, motor.
Introducción
En ciertas aplicaciones prácticas es necesario, por cuestiones de seguridad, comodidad, disposición física, etc. comandar motores a distancia evitando el cableado entre el módulo de control, accionado por el operario, y los mismos. Este objetivo se logra transmitiendo las señales de control mediante ondas electromagnéticas a una determinada frecuencia y codificando ésta información con distintas técnicas (AM, FM, ASK, FSK, etc). Este tipo de transmisión es denominada Inalámbrica y tiene, para este trabajo, la particularidad de ser unidireccional.
Este sistema se denomina de lazo abierto debido a que cuando desde el Módulo de Control (MC) se establece una velocidad determinada por el motor, no existe ningún mecanismo de sensado de la señal de salida (en este caso la velocidad) que realimente la misma para corregir posibles errores.
La implementación del sistema de control a distancia propuesta puede dividirse en tres etapas: 1-Interfaz de Usuario 2-Lógica de control 3-Transmisión/Recepción Inalámbrica 4-Conversión Digital/Analógica 5-Controlador de Potencia del motor.
En el siguiente diagrama se muestra la interconexión de las etapas mencionadas:

Descripción por Etapas

Interfaz de Usuario

Esta sencilla etapa consta de tres pulsadores, uno para resetear el módulo y los otros dos para incrementar o decrementar la velocidad del motor en uno de los sentidos. Además consta de 2 LEDs que indican cuando ha sido alcanzada la máxima velocidad de rotación en cualquiera de los dos sentidos.
Se cuenta con la posibilidad, mediante un jumper, de dejar fija la habilitación para la transmisión de datos, o controlarla mediante uno de los pines del PIC.

Lógica de control

Al iniciarse o resetearse el Firmware del PIC16F84 utilizado, una variable interna del mismo llamada VEL se encuentra en el valor decimal 8, que equivale al estado de reposo del motor. Los valores para VEL desde de 0 a 7, corresponden a distintas velocidades de giro en un sentido, siendo el 0 la máxima y 7 la mínima. En el otro sentido, 9 equivale a la mínima velocidad, y 15 a la máxima. Al presionar los pulsadores de velocidad, el firmware modifica VEL, incrementándola o decrementándola. Inmediatamente después, el Firmware Actualiza sus salidas de acuerdo al nuevo valor de VEL, con lo que éste se transmite hacia el controlador del motor. Si se alcanzan los valores extremos de VEL (0 o 15), esto se indicará mediante el encendido de uno de los LEDs.

Transmisión/Recepción Inalámbrica

Conversión Digital/Analógica

Controlador de Potencia

 Estos datos de los pulsadores son enviados al PIC16F84. El cual envía los 4 bits mas significativos de la información a la siguiente etapa.
Para la transmisión de datos usamos el módulo TWS-BS3

Page Layout
Your paper must use a page size corresponding to A4 which is 210mm (8.27") wide and 297mm (11.69") long. The margins must be set as follows:
- Top = 19mm (0.75")
- Bottom = 43mm (1.69")
- Left = Right = 14.32mm (0.56")
Your paper must be in two column format with a space of 4.22mm (0.17") between columns.
Page Style
All paragraphs must be indented. All paragraphs must be justified, i.e. both left-justified and right-justified.
Text Font of Entire Document
The entire document should be in Times New Roman or Times font. Type 3 fonts must not be used. Other font types may be used if needed for special purposes.
Recommended font sizes are shown in Table 1.
Title and Author Details
Title must be in 24 pt Regular font. Author name must be in 11 pt Regular font. Author affiliation must be in 10 pt Italic. Email address must be in 9 pt Courier Regular font.

TABLE I
Font Sizes for Papers
Font Size	Appearance (in Time New Roman or Times)
	Regular	Bold	Italic
8	table caption (in Small Caps), / figure caption, / reference item		reference item (partial)
9	author email address (in Courier), / cell in a table	abstract body	abstract heading (also in Bold)
10	level-1 heading (in Small Caps), / paragraph		level-2 heading, / level-3 heading, / author affiliation
11	author name
24	title

All title and author details must be in single-column format and must be centered.
Every word in a title must be capitalized except for short minor words such as “a”, “an”, “and”, “as”, “at”, “by”, “for”, “from”, “if”, “in”, “into”, “on”, “or”, “of”, “the”, “to”, “with”.
Author details must not show any professional title (e.g. Managing Director), any academic title (e.g. Dr.) or any membership of any professional organization (e.g. Senior Member IEEE).
To avoid confusion, the family name must be written as the last part of each author name (e.g. John A.K. Smith).
Each affiliation must include, at the very least, the name of the company and the name of the country where the author is based (e.g. Causal Productions Pty Ltd, Australia).
Email address is compulsory for the corresponding author.
Section Headings
No more than 3 levels of headings should be used. All headings must be in 10pt font. Every word in a heading must be capitalized except for short minor words as listed in Section III-B.
1. Level-1 Heading: A level-1 heading must be in Small Caps, centered and numbered using uppercase Roman numerals. For example, see heading “III. Page Style” of this document. The two level-1 headings which must not be numbered are “Acknowledgment” and “References”.
2. Level-2 Heading: A level-2 heading must be in Italic, left-justified and numbered using an uppercase alphabetic letter followed by a period. For example, see heading “C. Section Headings” above.
3. Level-3 Heading: A level-3 heading must be indented, in Italic and numbered with an Arabic numeral followed by a right parenthesis. The level-3 heading must end with a colon. The body of the level-3 section immediately follows the level-3 heading in the same paragraph. For example, this paragraph begins with a level-3 heading.
Figures and Tables
Figures and tables must be centered in the column. Large figures and tables may span across both columns. Any table or figure that takes up more than 1 column width must be positioned either at the top or at the bottom of the page.
Graphics may be full color. All colors will be retained on the CDROM. Graphics must not use stipple fill patterns because they may not be reproduced properly. Please use only SOLID FILL colors which contrast well both on screen and on a black-and-white hardcopy, as shown in Fig. 1.

Fig. 1 A sample line graph using colors which contrast well both on screen and on a black-and-white hardcopy

Fig. 2 shows an example of a low-resolution image which would not be acceptable, whereas Fig. 3 shows an example of an image with adequate resolution. Check that the resolution is adequate to reveal the important detail in the figure.
Please check all figures in your paper both on screen and on a black-and-white hardcopy. When you check your paper on a black-and-white hardcopy, please ensure that:
- the colors used in each figure contrast well,
- the image used in each figure is clear,
- all text labels in each figure are legible.
Figure Captions
Figures must be numbered using Arabic numerals. Figure captions must be in 8 pt Regular font. Captions of a single line (e.g. Fig. 2) must be centered whereas multi-line captions must be justified (e.g. Fig. 1). Captions with figure numbers must be placed after their associated figures, as shown in Fig. 1.

Fig. 2 Example of an unacceptable low-resolution image

Fig. 3 Example of an image with acceptable resolution

Table Captions
Tables must be numbered using uppercase Roman numerals. Table captions must be centred and in 8 pt Regular font with Small Caps. Every word in a table caption must be capitalized except for short minor words as listed in Section III-B. Captions with table numbers must be placed before their associated tables, as shown in Table 1.
Page Numbers, Headers and Footers
Page numbers, headers and footers must not be used.
Links and Bookmarks
All hypertext links and section bookmarks will be removed from papers during the processing of papers for publication. If you need to refer to an Internet email address or URL in your paper, you must type out the address or URL fully in Regular font.
References
The heading of the References section must not be numbered. All reference items must be in 8 pt font. Please use Regular and Italic styles to distinguish different fields as shown in the References section. Number the reference items consecutively in square brackets (e.g. [1]).
When referring to a reference item, please simply use the reference number, as in [2]. Do not use “Ref. [3]” or “Reference [3]” except at the beginning of a sentence, e.g. “Reference [3] shows …”. Multiple references are each numbered with separate brackets (e.g. [2], [3], [4]–[6]).
Examples of reference items of different categories shown in the References section include:
- example of a book in [1]
- example of a book in a series in [2]
- example of a journal article in [3]
- example of a conference paper in [4]
- example of a patent in [5]
- example of a website in [6]
- example of a web page in [7]
- example of a databook as a manual in [8]
- example of a datasheet in [9]
- example of a master’s thesis in [10]
- example of a technical report in [11]
- example of a standard in [12]
Conclusions
The version of this template is V2. Most of the formatting instructions in this document have been compiled by Causal Productions from the IEEE LaTeX style files. Causal Productions offers both A4 templates and US Letter templates for LaTeX and Microsoft Word. The LaTeX templates depend on the official IEEEtran.cls and IEEEtran.bst files, whereas the Microsoft Word templates are self-contained. Causal Productions has used its best efforts to ensure that the templates have the same appearance.
Causal Productions permits the distribution and revision of these templates on the condition that Causal Productions is credited in the revised template as follows: “original version of this template was provided by courtesy of Causal Productions (www.causalproductions.com)”.
Acknowledgment
The heading of the Acknowledgment section and the References section must not be numbered.
Causal Productions wishes to acknowledge Michael Shell and other contributors for developing and maintaining the IEEE LaTeX style files which have been used in the preparation of this template. To see the list of contributors, please refer to the top of file IEEETran.cls in the IEEE LaTeX distribution.
References
1. S. M. Metev and V. P. Veiko, Laser Assisted Microtechnology, 2nd ed., R. M. Osgood, Jr., Ed. Berlin, Germany: Springer-Verlag, 1998.
2. J. Breckling, Ed., The Analysis of Directional Time Series: Applications to Wind Speed and Direction, ser. Lecture Notes in Statistics. Berlin, Germany: Springer, 1989, vol. 61.
3. S. Zhang, C. Zhu, J. K. O. Sin, and P. K. T. Mok, “A novel ultrathin elevated channel low-temperature poly-Si TFT,” IEEE Electron Device Lett., vol. 20, pp. 569–571, Nov. 1999.
4. M. Wegmuller, J. P. von der Weid, P. Oberson, and N. Gisin, “High resolution fiber distributed measurements with coherent OFDR,” in Proc. ECOC’00, 2000, paper 11.3.4, p. 109.
5. R. E. Sorace, V. S. Reinhardt, and S. A. Vaughn, “High-speed digital-to-RF converter,” U.S. Patent 5 668 842, Sept. 16, 1997.
6. (2002) The IEEE website. [Online]. Available: http://www.ieee.org/
7. M. Shell. (2002) IEEEtran homepage on CTAN. [Online]. Available: http://www.ctan.org/tex-archive/macros/latex/contrib/supported/IEEEtran/
8. FLEXChip Signal Processor (MC68175/D), Motorola, 1996.
9. “PDCA12-70 data sheet,” Opto Speed SA, Mezzovico, Switzerland.
10. A. Karnik, “Performance of TCP congestion control with rate feedback: TCP/ABR and rate adaptive TCP/IP,” M. Eng. thesis, Indian Institute of Science, Bangalore, India, Jan. 1999.
11. J. Padhye, V. Firoiu, and D. Towsley, “A stochastic model of TCP Reno congestion avoidance and control,” Univ. of Massachusetts, Amherst, MA, CMPSCI Tech. Rep. 99-02, 1999.
12. Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specification, IEEE Std. 802.11, 1997.