Pin #	Pin Name	SD Signal Function SD Mode	SPI Signal Function SPI Mode
1	DAT3/CS	Data Line 3	Chip Select/Slave Select [SS]
2	CMD/DI	Command Line	Master Out/Slave In [MOSI]
3	VSS1	Ground	Ground
4	Vdd	Voltage Supply [2.7v or 3.6v]	Voltage Supply [2.7v or 3.6v]
5	Clock	Clock	Clock [SCK]
6	Vss2	Ground	Ground
7	DAT0/D0	Data Line 0	Master In Slave Out [MISO]
8	DAT1/IRQ	Data Line 1	Unused or IRQ
9	DAT2/NC	Data Line 2	Unused